## Slide 1
Task Risk Assessment

## Slide 2
ICE BREAK

## Slide 3
The TRA process
Risk assessment is a structured process whereby hazards present in a workplace
are identified, evaluated
and corrective action(s) prioritized
in order to reduce risks to acceptable levels.

## Slide 4: SO THAT...
WE CAN CONTINUALLY
IMPROVE OUR SAFETY STANDARDS
AND OUR JOURNEY
TO A ZERO INURY RATE
CAN BE REALIZED and SUSTAINED
REWORD

## Slide 5
The TRA Process
Elimination of the most significant hazards
Fulfill Regulatory & Policy requirements
Involves teams from all levels
Is focused on the actual work activity
Improved awareness of hazards and/ or identify new ones.
Ensure the correct “control measures” are in place and reflected in job procedures,
Continuously improve Safety systems and conditions of work
Reduce incidents
Benefits & Strengths:

## Slide 6
When it should be used
Proper safety procedures are identified as not being in place
Existing procedures are not adequate
New job, task, chemical, machine has been introduced
Existing task has been significantly changed
New/ different people doing the task
Specific Regulatory or Company requirement
Change in standards
Changes in technology
Unplanned work
To continue work after an incident or injury has occurred
Result of medical surveillance
When….

## Slide 7: When do you apply?
    Electrical Work
    D&R Work
    High pressure cleaning
    Confined space Entry
    Line Break
    Working at heights
    Deviations from SHE procedures and SOP’s
    Rigging & Hoisting
    Hot Work (flames / sparks)
  New tasks/jobs
  Details job not known
  Dangerous chemicals involved
  Other jobs in same area
  Contractor work
  Jobs with > 1 person
  non barricaded area
  not familiar with the job ?
EXAMPLES:

## Slide 8
For tasks where the hazards/risks
are obvious
and well known
and clearly understood.
Typically this is the case for jobs
for which we have SOP’s.
When is it NOT required?

## Slide 9: TRA Procedure/ Training Overview
TRA technique is to be applied for General Safety,,,,
not intended to be used to classify hazards or risks associated with
Process Safety Management.

## Slide 10: TRA TRAINING PACKAGE
1. Reasons, study purposes
2. Hazard & Risk
3. Hazard Categories
4. Existing safety measures and strategy processes
5. Walk-through form
6. Checklist

## Slide 11: Training Covers the:
Purpose?
Who?
What?
Where?
When?
How?
Examples
Exercise

## Slide 12: Guidelines of Training Workshop:
Successfully Delivered In a way that :
Priority can be given to the execution of a TRA.
One knows when a TRA should be applied.
One is capable of :
  doing a TRA
  documenting a TRA
  preparing a plan of action
  discussing
One can decide who is needed for the TRA.

## Slide 13: You don’t need to study for this!
Assessing risks is something
people do naturally but
you do need to gain experience
You don’t need
to be a scientist or a professor
to do this!

## Slide 14
- Dividing of jobs into sub-tasks
- Identifying hazards
- Evaluate the risk
- Implement measures that will eliminate or minimize risks
- Take action on important findings
  These need to be brought back to acceptable levels
What constitutes a TRA?

## Slide 15
Hazard & Risk

## Slide 16: DEFINITIONS
Hazard
……something that can cause injury or damage to ones health.
Risk
the likelihood that an injury will occur

## Slide 17: EXAMPLE OF HAZARDS & RISKS
Activity: CROSSING A BUSY ROAD
Hazard = Being hit by a car
Risk = Actual chance of being hit and injured
Frequency of Exposure :
- do you do it every year, month, day, every hour?
Severity:
possible serious or fatal injury
Probability:
- the practical chance that it will happen

## Slide 18: Calculation Method
RISK = Exposure x Severity x Probability

## Slide 19
HAZARD CATEGORIES
PHYSICAL
CHEMICAL
ERGONOMIC
BIOLOGICAL
ENVIRONMENTAL

## Slide 20
PHYSICAL HAZARDS
ELECTRICAL,
RADIATION,
SOUND, VIBRATION,
MECHANICAL/MACHINES,
FALLING (OBJECTS & PEOPLE)
FIRE

## Slide 21
CHEMICAL HAZARDS
LIQUIDS, GASSES, SOLIDS
Enter the body by means of :
SWALLOWING (mouth)
ABSORBTION (skin)
INHALING (airways)

## Slide 22
CHEMICAL HAZARDS :
EXPLOSIVE
OXIDATION
FLAMMABLE
POISONOUS
CHEMICAL BURNING
IRRITATION
SENSITIVITY
CANCER CAUSING
MUTATION
REPRODUCTIVE

## Slide 23
ERGONOMIC HAZARD
BACK INJURY
HAND, WRIST, ARM, NECK STRESS AS A RESULT OF COMPUTER USE
UNCOMFORTABLE POSITIONS WHICH CAUSE STRESS TO THE MUSCLES
INJURY DUE TO OVER EXERSION
MUSCLE TEARING

## Slide 24
BIOLOGICAL HAZARDS
HEPATITIS,
HIV-INFECTED
LEGIONNAIRES DISEASE
This is a highly specialized area where health care professionals should be consulted

## Slide 25
ENVIRONMENTAL HAZARDS
- EMISSIONS
- SPILLS
- PRODUCTS THAT POLLUTE
THE EARTH
- GROUND WATER
- WASTE IN GENERAL

## Slide 26
EVALUATING PROTECTION via EXISTING SAFETY MEASURES

## Slide 27: Existing Safety Measures
Safety rules, procedures & manuals
Operating procedures
Permit systems
(LTCT, confirmed space, hotwork etc)
Monitoring & sampling
Auditing
Training/information/instruction
Supervision
Emergency Plans
Personal protective equipment (PPE)

## Slide 28: Action Plans are needed if:
There is insufficient control on the basis
of the hazard with existing safety measures.

## Slide 29: TRA - Task Risk Assessment
This is a methodology to identify and evaluate the hazards and risks in a systematic and quantitative way.
The system used is often referred to as “Kinney and Fine”, two European researchers.

## Slide 30: BASIC TRA STEPS:
Identify task and sub-tasks
Calculate initial Risk-Score
Define measure(s)
Include standard and additional measures. Always take prevention hierarchy into account (see next slide)
Calculate Actual-Risk
Acceptable ?
Implement measure(s)
File Risk Analysis
Identify Hazard
N

## Slide 31: Prevention Hierarchy for control measures
1. Elimination: Eliminate Risk
2. Substitution: Reduce Risk at source
or remove source
3. Engineering Control: Take collective measures
4. Administrative Control: Training + procedures
+ instructions
5. PPE: Make people wear PPE

## Slide 32: Risk Score with Kinney & Fine
RISK = Exposure x Severity x Probability
R = E X S X P

## Slide 33
Exposure:

## Slide 34
Severity:

## Slide 35
Probability:

## Slide 36: Risk Score Interpretation:

## Slide 37: Walk-through form & Checklist
Walk through
TRA checklist

## Slide 38: Pit-falls
Always do it in group.
  Group results are more stable than results of individuals.
If R<20, we still can decide to take measures based on common sense.
  e.g; Low Frequency x High Severity x Low Probability
Not re-calculating score after corrective actions have been developed
Undertaking a risk assessment to try to justify a decision that already has been taken.
Undertaking a detailed quantified risk assessment without considering if relevant good practice was available
Not identifying all hazards associated with the activities
Failure to fully & truly consider all potential outcomes
Not linking hazards with risk controls.
Not being familiar with the situation in the field

## Slide 39
Questions ?

## Slide 40: Exercise 1: fix the tires of your bike
Individually: list all the subtasks you see relative to the job

## Slide 41: Example 1: Electrical cabinet
Evaluate need for measures for electrical work in an MCC. The Risk is getting burned by electrical arc.
Initial Risk
E = 1
S = 15
P = 3
R = 45
Measures
full PPE
procedures
Actual Risk 1
E = 1
S = 7
P = 5
R = 35
Additional Measures (since R>20)
Trained standby-man for immediate alarm and isolation of victim to minimise potential injury + current limiting fuse.
Actual Risk 2
E = 1 S = 4 P = 3
R = 12 (acceptable situation)

## Slide 42: Exercise 2: Cut straps on bags
Try to evaluate with what kind of knife the bags must be cut open and how ...

## Slide 43
The knives

## Slide 44: Risk is to cut fingers/hand/bodyparts
Evaluation: If one uses the knive with wooden handle and leather gloves, what is the risk to cut yourself and how would you improve the situation

## Slide 45: Initial Risk
Initial Risk
E = 7
S = 7
P = 6
R = 294
Measures 1
Kevlar® gloves
Safety knife with spring loaded retractable blade
Procedure: Cut away from body

## Slide 46: New Situation
Actual Risk 1
E = 7
S = 3
P = 3
R = 63
Measures 2
Kevlar® gloves
Side Cutter

## Slide 47: End Result
Actual Risk 2
E = 7
S = 1
P = 2.5
R = 17.5
R < 20 AND S < 4 ……… This is an acceptable situation

## Slide 48
For the safe world,
work together for the one world.