## Slide 1
“If you want to become a chemist, you have to ruin your health. Who does not ruin his health by his studies, nowadays will not get anywhere in Chemistry”
-August Kekule (1890)

## Slide 2: Chemical Management : Curriculum, Sensitization and Methodologies (in the Academe)
AILEEN MAY G. ANG, R.Ch.
Central Mindanao University
Musuan, Bukidnon, Philippines
Seminar on the Chemical Weapons Convention and Chemical
Safety and Security Management for Member States
of the OPCW in the Asia Region
Doha Regional Centre for CBRN Training, Doha, Qatar
4-6 February 2020

## Slide 3: Objectives:
Understand the importance of chemical management in schools
Familiarize the components/framework of chemical management
Identify measures to make people realize the importance of chemical management
Determine steps how to put chemical management plan into action

## Slide 4: Are there dangerous chemicals in your school?
Source: EPA. 2006. Chemical Resource Management Guide for School Administrators.
www. Google.com (images)
Laboratory chemicals
Inks, paints, and degreasers for industrial arts
Pesticides and Fertilizers
Maintenance Supplies
Healthcare Equipment

## Slide 5
Why chemical management should be a concern in schools?
Improper chemical management poses health and safety risks to students and school employees
Expenses incurred from disposal, spills, and other incidents

## Slide 6
Why chemical management should be a concern in schools?
It only takes one chemical incident, such as a spill, explosion, or chemical exposure, to BREAK THE TRUST WITH THE COMMUNITY
Improper chemical management may result in school closures that result in a loss of valuable education time.

## Slide 7
Why chemical management should be a concern in schools?
Improper chemical management can lead to unintended chemical discharges and spills, which inflict damage upon the environment

## Slide 8: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
A
D
M
I
N
I
S
T
R
A
T
O
R
S
What is the minimum amount of this chemical that is needed to perform the experiment? (When ordering chemicals, less is always best
Is the proper PPE available in the laboratory to handle this chemical?
What are the special handling precautions?
Where will the chemical be stored in the laboratory? Does the laboratory chemical hood provide proper ventilation?
Are there special containment considerations in the event of a spill, fire, or flood?
Will there be additional costs or considerations related to the disposal of this chemical?

## Slide 9: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
Before a substance is received, information on proper handling, storage, and disposal should be known to those who will be involved
No container should be accepted without an adequate identifying label
All substances should be received in a central location
Personnel should be trained to identify signs of breakage (e.g., rattling) and leakage (e.g., wet spot or stain) on shipments and such shipments should be refused or opened in a hood by laboratory staff
A
D
M
I
N
I
S
T
R
A
T
I
O
N

## Slide 10: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
Laboratory personnel should separate and store all chemicals according to hazard category and compatibility
Laboratory personnel should read the MSDS and consider the precautions regarding the storage requirements of the chemicals in the laboratory
All chemical containers must be properly labeled with the full chemical name
Rooms used for chemical storage and handling should be controlled-access areas

## Slide 11: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
comprehensive file of MSDS must be kept in the laboratory or be readily accessible online to all employees during all work shifts

## Slide 12: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
Stored chemicals should be examined periodically (at least annually) for replacement, deterioration, and container integrity
Periodic inventories should be conducted, with unneeded items being discarded or returned to the storeroom/stockroom

## Slide 13: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
use a secondary containment device or carts
Avoid high-traffic areas when moving chemicals within the building

## Slide 14: Chemical Management: Components
Chemical Procurement
Chemical Storage
Chemical Handling
Chemical Inventory
Transferring of Chemicals
Waste Disposal
All chemical waste must be stored and disposed of in compliance with applicable federal, state, local, and institutional regulatory requirements
Waste containers should be properly labeled

## Slide 15: Chemical Management: Sensitization
Significant Findings:
levels of awareness ranged between fair to good for the majority of assessment criteria
students have shown poor attitude towards safety in chemical laboratories
weakness on how staff deal with specific emergency incidents
Recommendations:
Improve the culture of safety ethics and risk management among the university staff and students by establishing an Environmental Health and Safety Office
Develop a course on hazardous waste and risk management, to be made compulsory for all university students

## Slide 16: Chemical Management: Sensitization
Publicize Chemical Management Program/Plan
Develop and Deliver Effective Message/Slogan
Integrate Chemical Management in the Course or Program Curriculum
Identify Target Audiences and hold awareness seminar
Use existing communication channel to publicize program
Update the technical “know-how” of the faculty and staff

## Slide 17: Chemical Management: Sensitization
Publicize Chemical Management Program/Plan
Develop and Deliver Effective Message/Slogan
develop a message that is distinctive, clear, simple, and compelling
develop a catchy program name or slogan -- help your program make a memorable splash and maintain interest
Sample Slogans:
Rehab the Lab!
Safer School…. Healthy School!
Safer Schools Initiative”

## Slide 18: Chemical Management: Sensitization
Publicize Chemical Management Program/Plan
Identify Target Audiences and hold awareness seminar
Tailoring your central message to each target audience increases your chances of gaining support for your program
think about which program components should be emphasized
Target Audience | Program Component | Sample “Hot” Topic
Administrator | Purchasing, Storage, Inventory, Use, Disposal | Liability and Budget
Faculty and Staff | Storage, Inventory, Use, Disposal | Classroom safety, curriculum, and professional responsibility
Students | Storage, Use, Disposal | Danger Imposed by Chemicals and Safety Measures
Parents | Storage, Disposal | Their Children’s Health

## Slide 19: Chemical Management: Sensitization
Publicize Chemical Management Program/Plan
Use existing communication channel to publicize program
use existing approaches and products
No need to reinvent the “wheel”

## Slide 20: Chemical Management: Sensitization
Publicize Chemical Management Program/Plan
CONSIDER THE MOST EFFECTIVE TIME OF YEAR TO PERFORM COMMUNICATION AND PUBLICITY EFFORTS
“Timing is everything”
Pick a time that will optimize participation, funding, and results
Stakeholders may be more receptive near the beginning of the school year when students are settled and ‘back-to-school’ is still on the public’s mind
A chemical inventory or cleanout might be safer if it is carried out during summer months when fewer students, teachers, and staff are present

## Slide 21: Chemical Management: Sensitization
Update the technical “know-how” of the faculty and staff
budget for seminars and trainings (e.g. annual faculty conference)
“Capacity building”
Integrate chemical management in the course curriculum

## Slide 22: Chemical Management: Sensitization
Integrate chemical management in the course curriculum

## Slide 23: Chemical Management: Methodologies
A. Create an institutional safety and security committee and appoint chemical safety and security officers
Chemical safety
Chemical inventory
First aid
Emergency Measures
Chemical Security
Chemical Waste Disposal
B. Evaluate current chemical management practices
Conduct a visual tour to get first impressions of chemical management situation, policies, and practices

## Slide 24: Chemical Management: Methodologies
B. Evaluate current chemical management practices
Perform a comprehensive evaluation of chemical management situation, policies, and procedures
Purchasing
Storage
Inventory

## Slide 25: Chemical Management: Methodologies
B. Evaluate current chemical management practices
Perform a comprehensive evaluation of chemical management situation, policies, and procedures
Use
Disposal

## Slide 26: Chemical Management: Methodologies
C. Develop a safety and security policy statement and implement administrative controls or modify existing chemical management procedures
define, document, and endorse a chemical safety and security management system
Implement institution’s rules and procedures and establish the responsibilities of individuals
Controls (general safety rules, laboratory housekeeping procedures, waste disposal etc.)
E. Train appropriate groups on responsible chemical management
ALL that is involved in the school chemical management aspect are all candidates for the training
administrators
faculty
staff
Parents
Students

## Slide 27: Chemical Management: Methodologies
E. Train appropriate groups on responsible chemical management

## Slide 28: Chemical Management: Methodologies
F. Perform an inventory of all chemicals and chemical products
Important to:
  making responsible purchasing decisions
  considering safe storage arrangements
  evaluating use
  estimating removal and disposal cost
Chemical inventory include:
  Chemical or product name
  Place(s) where material is being stored (room, name, building);
  Program(s) using the material and whether it is currently being used
  Date of purchase
  Amount of material currently in school (by location).

## Slide 29: Chemical Management: Methodologies
F. Perform an inventory of all chemicals and chemical products

## Slide 30: Chemical Management: Methodologies
G. Segregate waste properly and secure a chemical cleanout professional
Segregate waste properly as indicated in the Safety Manual and Laboratory Manual and during class orientation
Evaluate your chemical inventory and create a list of chemicals to dispose (a disposal list)
Identify a qualified professional(s) to assist in the cleanout and disposal process (Third party)

## Slide 31: Chemical Management: Methodologies
H. Implement a “green” curriculum: Green Chemistry for Every Laboratory
Green Chemistry philosohy of designing products and processes that reduce or eliminate the use and generation of hazardous substances
  Reducing chemicals in the school’s operational aspect (janitorial/sanitation)
  Apply 12 principles of green chemistry for prudent experiment design and execution

## Slide 32: Chemical Management: Methodologies
H. Implement a “green” curriculum: Green Chemistry for Every Laboratory

## Slide 33
H. Implement a “green” curriculum: Green Chemistry for Every Laboratory
Heating Device | Time (min) | Energy Consumed (KJ) | Energy Saved (KJ)
Microwave Oven | 2 | 51 | 75.0%
Hot Plate | 14 | 288 | 
Design for energy efficiency

## Slide 34
H. Implement a “green” curriculum: Green Chemistry for Every Laboratory
Less Hazardous Chemical Synthesis/ Benign solvent for natural products Extraction

## Slide 35
H. Implement a “green” curriculum: Green Chemistry for Every Laboratory
Waste Reduction/Prevention: Design of micro-scale experiments

## Slide 37
ACKNOWLEDGMENT:
DR. ANN P. VILLALOBOS
Research Fellow & Consultant, Janssen Pharmaceuticals
Research company of
Johnson & Johnson Company (USA)
ENGR. EMMIE G. REYES
ASEAN Engineer
College of Engineering,
Central Mindanao university,
Bukidnon,
Philippines
EPA. 2006. Chemical Resource Management Guide for School Administrators.
EPA. 2008. Building a successful program to address chemical risks in school: A Workbook with Templates, Tips and Techniques. http://www.epa.gov/sc3
National Research Council. (2011). Prudent practices in the laboratory: handling and management of chemical hazards, updated version. National Academies Press.